## Slide 1: Fabrics & Stabilizers
FTCU Masterclass by D.J. Anderson
DEEP
DIVE

## Slide 2: 3 Components of Embroidery
Fabric
  Type and Properties
Design
  Size, Style, and Number of Stitches
Stabilizer
  Type and Amount

## Slide 3: 3 Components of Embroidery
What Component Do You Think Dictates What We Need To Do Overall for our Embroidery?
How Do You Get Everything Right?

## Slide 4: Fabrics
How fabrics dictate stabilizer and design properties
Categories of fabrics
Fabric Stabilizer Guide

## Slide 5: Fabrics Role
Underlay, density, stitch length, stitch direction, needle to use, and stabilizer are all determined by the fabric you are stitching the design onto.
the fabric is the most important component to the embroidery process
 | What we do to accommodate for the fabric
Design | We modify the properties (stitch length, density, underlay, push and pull compensation) of each object in the design that work best for the fabric we will be embroidering the design onto.
Stabilizer | We choose the base stabilizer that is necessary to best stabilize fabric for the design.
Needle | We choose the base needle type (style, size and point type) that works best with the fabric we will be embroidering onto.
Hooping | We choose the hooping technique that is best for the given fabric type. Some fabrics cannot be hooped. We always hoop when we can for optimal performance.

## Slide 6: Fabric Categories
Knit Fabrics (fabrics with stretch)
Woven Fabrics (stable fabrics that don’t stretch)
Sheer Fabrics (fabrics can see through)
Non-Fabric Materials (manmade and leathers)
Notes: Add an image that signifies stretching and no stretching and add Knit and Woven at the top. Show a Sheer Fabric. Non-Fabric Material.

## Slide 7: Knit Fabrics
We need to minimize their stretch and prevent the fabric from moving as much as possible.
We need to use a Cutaway stabilizer when embroidering on knits.
It is best to use a Fusible Cutaway stabilizer to minimize stretch and movement the most.
My Preferred Cutaway Stabilizer: Floriani Power Mesh Fusible

## Slide 8: Woven Fabrics
Because they are more stable in nature than knit fabrics, we can use lighter amounts of underlay and stitch properties in a design.
We generally use a Tearaway stabilizer for woven fabrics.
You can use a standard or fusible tearaway.
My preferred Tearaway: Floriani Heat N Stay

## Slide 9: Sheer Fabrics
Because you can see through these fabrics, we have to be more careful with our stabilizer choices.
Most Sheer Fabrics are woven; however, we can’t always use a tearaway stabilizer with them. If the design is solid with no big open areas, we can use a tearaway. If the design has a lot of open areas, we must use a fiber-based water-soluble stabilizer, so the stabilizer doesn’t ghost through the fabric.
My preferred stabilizer: Floriani Wet N Gone (fusible or tacky)

## Slide 10: Non-Fabric Materials
Examples: Leather, Faux Leather, Suede, and Vinyl
Many make the mistake of stabilizing them as if they are woven fabrics.
While they may seem to be stable materials because of their weight and/or thickness, they are far from it. They are spongy and need extra support as a result. Another challenge they present is that they can perforate easily. It is easy to cut a hole in these materials.
It is important to use a Cutaway Stabilizer with these materials
My preferred stabilizer: Floriani Perfect Stick Cutaway

## Slide 11: Stabilizer Type Based on Fabric
Knit Fabric (cutaway)
Standard: No-Show Mesh, Power Mesh, Cutaway Medium
Fusible: No-Show Mesh Fusible, Power Mesh Fusible, Cutaway Medium Fusible
Sticky: Perfect Stick Cutaway
Solid Woven Fabric (tearaway)
Standard: Tearaway Medium or Stitch N Wash
Fusible: Heat N Sta or Stitch N Wash Fusible
Sticky: Perfect Stick Tearaway
Sheer Woven Fabric (water soluble)
Standard: Wet N Gone
Fusible: Wet N Gone Fusible
Sticky: Wet N Gone Tacky
Non-Fabric (cutaway)
Sticky: Perfect Stick Cutaway
Standard: Cutaway Medium

## Slide 13: Stabilizers

## Slide 14: Stabilizers
Fabric | We choose the core stabilizer (tearaway or cutaway) that is necessary to best stabilize fabric for the design.
Design | The amount (1, 2, or more pieces) of stabilizer needed to support the fabric is determined by the number of stitches in the design and size.
Hooping | We choose the hooping technique that is best for the fabric or material. Some fabrics cannot be hooped. We always hoop when we can for optimal performance.
What we do to determine proper stabilization
Stabilizers play a very important role in the embroidery process. They are necessary to provide the necessary support to the fabric for the stitches being placed on it. Fabrics are not able to support the stitches by themselves.

## Slide 15: Core Stabilizers
Tearaway Stabilizers
Standard Tearaway
  Floriani Tearaway Medium
  Floriani Stitch N Wash
Fusible Tearaway
  Floriani Heat N Sta
  Floriani Stitch N Wash Fusible
Sticky Tearaway
  Floriani Perfect Stick Tearaway
Cutaway Stabilizers
Standard Cutaway
  Floriani Cutaway Medium
  Floriani No-Show Mesh
  Floriani Power Mesh
Fusible Cutaway
  Floriani Cutaway Medium Fusible
  Floriani No-Show Mesh Fusible
  Floriani Power Mesh Fusible
Sticky Cutaway
  Floriani Perfect Stick Cutaway

## Slide 16: Specialty Stabilizer, Topper, & Fabric Prep
Specialty Stabilizer
Water Soluble Cutaway
  Floriani Wet N Gone
  Floriani Wet N Gone Fusible
  Floriani Wet N Gone Tacky
Toppers
  Floriani Water Soluble Topping
  Floriani Heat N Gone
Fabric Prep
Floriani Dream Weave
Floriani Dream Weave Ultra
Floriani Dream Weave Supreme

## Slide 17: How to Determine What Type of Stabilizer to Use

## Slide 18: How To Determine the Proper Amount of Stabilizer
What we need to know:
  How many stitches does one piece of the stabilizer hold?
  How many stitches are in the design?
  What are the characteristics of the design?

## Slide 19: Tearaway Stabilizers
For stable woven fabrics, like denim, twill, nylon, towels, and robes that don’t stretch.
Quality tearaway stabilizers will hold up to 8,000 stitches in a 4x4-inch area. Use additional pieces as necessary for the stitch count and design size.
Standard Tearaway Stabilizer
  (Floriani Tearaway Medium, Floriani Stitch N Wash)
Fusible Tearaway Stabilizer
  (Floriani Heat N Stay, Floriani Stitch N Wash Fusible)
Sticky Tearaway Stabilizer
  (Floriani Perfect Stick, Floriani Wet N Stick
Partially Water-Soluble Tearaway
  (Floriani Stitch N Wash, Stitch N Wash Fusible)

## Slide 20: Cutaway Stabilizers
We want to use a cutaway stabilizer when working with knit fabrics, like t-shirts, golf/polo shirts, and sweatshirts.
Quality cutaway stabilizers should be able to support around 12,000 stitches. Use additional pieces when needed. Nylon or Polyester Mesh cutaway stabilizers can support 6,000 to 8,000 stitches per piece.
Standard Cutaway Stabilizer
  (Floriani Cutaway Medium, No Show Nylon Mesh, Power Mesh)
Fusible Cutaway Stabilizer
  (Cutaway Medium Fusible, No Show Nylon Mesh Fusible, Power Mesh Fusible)
Sticky Cutaway Stabilizer
  (Perfect Stick Cutaway)

## Slide 21: Specialty Products
For Applique
  Floriani Applique Wonder
For Lace
  Floriani Wet N Gone, Wet N Gone Fusible, Wet N Gone Tacky
For 3D Embroidery
  Floriani Hi Loft Dimensional Topping and Stabilizer
Floriani Dream Weave Lineup
  Dream Weave (use to cover embroidery stitches, behind delicate fabrics like silk, satin, lame)
  Dream Weave Ultra (use on delicate fabrics you’ll be embroidering with large or dense designs - adds extra support)
  Dream Weave Supreme (adds extra support to lightweight, loosely woven, or delicate fabrics when embellishing with embroidery, applique, or quilting.
Floriani Heat N Stay Fusible Fleece
For Patches
  Floriani Press N Bond Thread
For a Template or Fussy Cutting Fabric
  Floriani Template Tearaway

## Slide 22: Embroidery Topping
Water soluble
  The most common topping is completely water soluble.
Heat soluble
  It will remove with the touch of an iron or heat press. Great for towels, knits, and velvet
Floriani Color Keep
  For Blocking Fabric from Changing the Color of Thread as it eliminates the “show through” of the background fabric. It’s also great for towels and terry cloth.

## Slide 23: Stabilizer Guides & Charts

## Slide 26: Fabric Support Options

## Slide 27: Knit Fabric: Hooped

## Slide 28: Knit Fabric: Not Hooped

## Slide 29: Woven Fabric: Hooped

## Slide 30: Woven Fabric: Not Hooped

## Slide 31: Sheer Fabric: Hooped

## Slide 32: Sheer Fabric: Not Hooped

## Slide 33: Non-Fabric Material

## Slide 34: RNK Stabilizer Guides
Stabilizer Workbook:
https://www.rnkdistributing.com/resources/workbooks-guides/FlorianiWorkbookStabilizer.pdf
Stabilizer Recommendations:
https://www.rnkdistributing.com/resources/workbooks-guides/floriani-stabilizer-guide.pdf
Stabilizer Trouble Shooting:
https://www.rnkdistributing.com/resources/workbooks-guides/Stabilizer-Trouble-Shooting.pdf
Quilt Reference Guide:
https://www.rnkdistributing.com/resources/workbooks-guides/quilters-guide.pdf
Embroidery Terms:
https://www.rnkdistributing.com/resources/workbooks-guides/EmbroideryTerms.pdf

## Slide 35: Save 2 Sew
Use Save2Sew for stabilization recommendations

## Slide 36: Thanks For Watching
Next Month’s Topic: Recipes for Success